## Slide 1: Advanced Behavior and Design of Steel Structure
Team 6 M11205310 劉映彤 M11205314 張原嘉
“

## Slide 2: TABLE OF CONTENTS
Model Information
Base Shear &
Lateral Seismic Force
Load Combinations
Section Inspection
Modal Analysis
Story Drifts
Nonlinear
PUSHOVER Analysis
Discussion & Suggestion
Section Selection
Design Details
Nonlinear
Time History Analysis
01
02
03
04
05
06
07
08
09
10
11

## Slide 3: Model Information 01
“

## Slide 4: Model Information
III
Los Angeles (LA) (34.051283, -118.246637)
RISK CATAGORY
LOCATION
D－Stiff Soil
SITE CLASS
Design Code: ASCE 7-16

## Slide 5: Model Information
Fixed-end moment-resisting frames (MRF).
OUTER
Story Height | Span Length | No. of Stories
13 ft | 23 ft | 10
Each floor has a 4×6 span configuration.
Pin-connected gravity frames.
INTERIOR

## Slide 6: Base Shear & Lateral Seismic Force 02
“
Seismic Parameter
Base Shear
Lateral Seismic Force

## Slide 7: Seismic Parameters
Parameters | Value | Reference
 | 1.927 | By ATC Website
 | 0.703 | By ATC Website
 | 1 | By ATC Website
 | 1.5 | By table 11.4-2, , Site Class D
 | 1.972 | By ATC Website
 | 1.055 | By equation
 | 1.315 | By ATC Website
 | 0.703 | By equation
 | 8 | By ASCE 7-16 , Steel special moment frames
 | 1.25 | By table 1.5-2, Risk category III, Seismic important factor
 | 5.5 | By ASCE 7-16 , Steel special moment frames
Parameters | Value | Reference
 | 1.927 | By ATC Website
 | 0.703 | By ATC Website
 | 1 | By ATC Website
 | 1.5 | 
 | 1.972 | By ATC Website
 | 1.055 | 
 | 1.315 | By ATC Website
 | 0.703 | 
 | 8 | By ASCE 7-16 , Steel special moment frames
 | 1.25 | By table 1.5-2, Risk category III, Seismic important factor
 | 5.5 | By ASCE 7-16 , Steel special moment frames

## Slide 8: Seismic Parameters
Structural Period (T)
1.375 sec
Spectral Response
Acceleration (Sa)
0.511g
(From ATC Hazards)

## Slide 9: Lateral Seismic Force
Story |  |  |  |  |  |  | 
10 | 1523.520 | 130.000 | 1665994.019 | 0.217 | 1650.500 | 532.834 | 
9 | 1523.520 | 117.000 | 1431846.159 | 0.186 | 1650.500 | 307.480 | 532.834
8 | 1523.520 | 104.000 | 1208826.134 | 0.157 | 1650.500 | 259.588 | 840.315
7 | 1523.520 | 91.000 | 997699.023 | 0.130 | 1650.500 | 214.250 | 1099.902
6 | 1523.520 | 78.000 | 799397.034 | 0.104 | 1650.500 | 171.666 | 1314.152
5 | 1523.520 | 65.000 | 615089.486 | 0.080 | 1650.500 | 132.087 | 1485.818
4 | 1523.520 | 52.000 | 446301.870 | 0.058 | 1650.500 | 95.841 | 1617.904
3 | 1523.520 | 39.000 | 295139.542 | 0.038 | 1650.500 | 63.379 | 1713.745
2 | 1523.520 | 26.000 | 164775.854 | 0.021 | 1650.500 | 35.385 | 1777.124
1 | 1523.520 | 13.000 | 60835.690 | 0.008 | 1650.500 | 13.064 | 1812.509
Base | 0.000 | 0.000 | 0.000 | 0.000 |  | 0.000 | 1825.573
Total | 15235.200 | 715.000 | 7685904.811 | 1.000 |  | 1825.573 | 14019.877
Story |  |  |  |  |  |  | 
10 | 1523.520 | 130.000 | 1665994.019 | 0.217 | 1650.500 | 532.834 | 
9 | 1523.520 | 117.000 | 1431846.159 | 0.186 | 1650.500 | 307.480 | 532.834
8 | 1523.520 | 104.000 | 1208826.134 | 0.157 | 1650.500 | 259.588 | 840.315
7 | 1523.520 | 91.000 | 997699.023 | 0.130 | 1650.500 | 214.250 | 1099.902
6 | 1523.520 | 78.000 | 799397.034 | 0.104 | 1650.500 | 171.666 | 1314.152
5 | 1523.520 | 65.000 | 615089.486 | 0.080 | 1650.500 | 132.087 | 1485.818
4 | 1523.520 | 52.000 | 446301.870 | 0.058 | 1650.500 | 95.841 | 1617.904
3 | 1523.520 | 39.000 | 295139.542 | 0.038 | 1650.500 | 63.379 | 1713.745
2 | 1523.520 | 26.000 | 164775.854 | 0.021 | 1650.500 | 35.385 | 1777.124
1 | 1523.520 | 13.000 | 60835.690 | 0.008 | 1650.500 | 13.064 | 1812.509
Base | 0.000 | 0.000 | 0.000 | 0.000 |  | 0.000 | 1825.573
Total | 15235.200 | 715.000 | 7685904.811 | 1.000 |  | 1825.573 | 14019.877

## Slide 10: Lateral Seismic Force
532.834 kips
307.480 kips
259.588 kips
214.250 kips
171.666 kips
132.087 kips
95.841 kips
63.379 kips
35.385 kips
13.064 kips

## Slide 11: Load Combinations 03
“

## Slide 12: Load Combinations
DL: 120psf, LL: 100psf, SDL: 0psf

## Slide 13: Load Combinations
COMBO | Load | COMBO | Load
0 | 1.4(DL) |  | 
1 | 1.4(DL + SPDL) |  | 
2 | 1.2(DL + SPDL) + 1.6LL |  | 
3 | 1.2(DL + SPDL) + 1.0LL + 1.0Ex+ | 11 | 0.9(DL + SPDL) + 1.0LL + 1.0Ex+
4 | 1.2(DL + SPDL) + 1.0LL + 1.0Ex- | 12 | 0.9(DL + SPDL) + 1.0LL + 1.0Ex-
5 | 1.2(DL + SPDL) + 1.0LL + 1.0Ey+ | 13 | 0.9(DL + SPDL) + 1.0LL + 1.0Ey+
6 | 1.2(DL + SPDL) + 1.0LL + 1.0Ey- | 14 | 0.9(DL + SPDL) + 1.0LL + 1.0Ey-
7 | 1.2(DL + SPDL) + 1.0LL - 1.0Ex+ | 15 | 0.9(DL + SPDL) + 1.0LL - 1.0Ex+
8 | 1.2(DL + SPDL) + 1.0LL - 1.0Ex- | 16 | 0.9(DL + SPDL) + 1.0LL - 1.0Ex-
9 | 1.2(DL + SPDL) + 1.0LL - 1.0Ey+ | 17 | 0.9(DL + SPDL) + 1.0LL - 1.0Ey+
10 | 1.2(DL + SPDL) + 1.0LL - 1.0Ey- | 18 | 0.9(DL + SPDL) + 1.0LL - 1.0Ey-

## Slide 14: Section Selection 04
“

## Slide 15: Section Selection
Story | Beam (in.) | Stress Ratio | Column (in.) | Ext. Col. | Int. Col.
 |  |  |  | Stress Ratio | 
10 | BH 36x18x1.3x1.75 | 0.056~0.090 | BH 36x30x1.5x2.4 | 0.049~0.057 | 0.075~0.085
9 |  | 0.100~0.135 |  | 0.062~0.067 | 0.090~0.099
8 |  | 0.154~0.183 |  | 0.078~0.088 | 0.130~0.136
7 |  | 0.204~0.231 |  | 0.097~0.111 | 0.165~0.170
6 |  | 0.248~0.272 |  | 0.123~0.140 | 0.195~0.197
5 |  | 0.283~0.304 | BH 36x32x1.5x2.4 | 0.208~0.233 | 0.204~0.205
4 |  | 0.307~0.326 |  | 0.265~0.295 | 0.222~0.224
3 |  | 0.314~0.337 |  | 0.325~0.359 | 0.239~0.244
2 |  | 0.299~0.326 |  | 0.383~0.422 | 0.259~0.268
1 |  | 0.236~0.262 |  | 0.431~0.475 | 0.298~0.303
Fixed-end moment-resisting frames (MRF).

## Slide 16: Section Selection
Story | Beam | Stress Ratio | Column | Stress Ratio
10 | W 12x136 | 0.131 ~ 0.204 | W 12x336 | 0.046 ~ 0.061
9 |  | 0.129 ~ 0.202 |  | 0.075 ~ 0.084
8 |  | 0.129 ~ 0.202 |  | 0.107 ~ 0.116
7 |  | 0.129 ~ 0.201 |  | 0.225 ~ 0.232
6 |  | 0.129 ~ 0.200 |  | 0.279 ~ 0.286
5 |  | 0.128 ~ 0.200 | W 14x370 | 0.305 ~ 0.312
4 |  | 0.128 ~ 0.200 |  | 0.355 ~ 0.361
3 |  | 0.128 ~ 0.199 |  | 0.406 ~ 0.412
2 |  | 0.128 ~ 0.199 |  | 0.462 ~ 0.472
1 |  | 0.128 ~ 0.198 |  | 0.506 ~ 0.522
Pin-connected gravity frames.

## Slide 17: Width-Thickness Ratio Inspection
 | Beam | Column
Flange |  | 
Web |  | 
 | Beam | Column
Flange |  | 
Web |  | 
According to AISC 341-16 Table D1.1 highly ductile members

## Slide 18: Width-Thickness Ratio Inspection
 |  | Beam |  |  |  | Column | 
 |  | Flange |  | Web |  | Flange | 
Story |  |  | Upper Limit |  | Upper Limit |  | Upper Limit
MRF | 6-10F | 5.142 | 7.348 | 25.00 | 59.013 | 6.670 | 7.348
 | 1-5F | 5.142 | 7.348 | 25.00 | 59.013 | 6.250 | 7.348
Gravity Frame | 6-10F | 4.960 | 7.348 | 13.79 | 59.013 | 2.263 | 7.348
 | 1-5F | 4.960 | 7.348 | 13.79 | 59.013 | 3.101 | 7.348
 |  | Beam |  |  |  | Column | 
 |  | Flange |  | Web |  | Flange | 
Story |  |  | Upper Limit |  | Upper Limit |  | Upper Limit
MRF | 6-10F | 5.142 | 7.348 | 25.00 | 59.013 | 6.670 | 7.348
 | 1-5F | 5.142 | 7.348 | 25.00 | 59.013 | 6.250 | 7.348
Gravity Frame | 6-10F | 4.960 | 7.348 | 13.79 | 59.013 | 2.263 | 7.348
 | 1-5F | 4.960 | 7.348 | 13.79 | 59.013 | 3.101 | 7.348
PASS!
PASS!
PASS!
Width-Thickness Ratio Inspection

## Slide 19: Column web inspection of MRF
Story |  |  | Compare with 0.114 |  |  | Upper/ Lower Limit
10 | 130.52 | 0.013 | Less | 20.800 |  | 58.210
9 | 284.54 | 0.030 | Less | 20.800 |  | 57.160
8 | 465.81 | 0.049 | Less | 20.800 |  | 56.000
7 | 672.54 | 0.071 | Less | 20.800 |  | 54.650
6 | 901.21 | 0.095 | Less | 20.800 |  | 53.180
5 | 1148.57 | 0.115 | Greater |  | 51.810 | 36.051
4 | 1408.74 | 0.142 | Greater |  | 51.260 | 36.051
3 | 1676.59 | 0.169 | Greater |  | 50.720 | 36.051
2 | 1941.36 | 0.195 | Greater |  | 50.190 | 36.051
1 | 2173.67 | 0.219 | Greater |  | 49.710 | 36.051
Story |  |  | Compare with 0.114 |  |  | Upper/ Lower Limit
10 | 130.52 | 0.013 | Less | 20.800 |  | 58.210
9 | 284.54 | 0.030 | Less | 20.800 |  | 57.160
8 | 465.81 | 0.049 | Less | 20.800 |  | 56.000
7 | 672.54 | 0.071 | Less | 20.800 |  | 54.650
6 | 901.21 | 0.095 | Less | 20.800 |  | 53.180
5 | 1148.57 | 0.115 | Greater |  | 51.810 | 36.051
4 | 1408.74 | 0.142 | Greater |  | 51.260 | 36.051
3 | 1676.59 | 0.169 | Greater |  | 50.720 | 36.051
2 | 1941.36 | 0.195 | Greater |  | 50.190 | 36.051
1 | 2173.67 | 0.219 | Greater |  | 49.710 | 36.051
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
Width-Thickness Ratio Inspection

## Slide 20: Column web inspection of gravity frames
Story |  |  | Compare with 0.114 |  |  | Upper/ Lower Limit
10 | 243.04 | 0.049 | Less | 6.110 |  | 56.000
9 | 485.71 | 0.099 | Less | 6.110 |  | 52.930
8 | 728.05 | 0.148 | Greater |  | 51.140 | 36.051
7 | 969.86 | 0.198 | Greater |  | 50.130 | 36.051
6 | 1212.6 | 0.247 | Greater |  | 49.140 | 36.051
5 | 1456.15 | 0.269 | Greater |  | 48.700 | 36.051
4 | 1700.11 | 0.315 | Greater |  | 47.770 | 36.051
3 | 1944.94 | 0.360 | Greater |  | 46.860 | 36.051
2 | 2196.97 | 0.407 | Greater |  | 45.910 | 36.051
1 | 2452.24 | 0.454 | Greater |  | 44.960 | 36.051
Story |  |  | Compare with 0.114 |  |  | Upper/ Lower Limit
10 | 243.04 | 0.049 | Less | 6.110 |  | 56.000
9 | 485.71 | 0.099 | Less | 6.110 |  | 52.930
8 | 728.05 | 0.148 | Greater |  | 51.140 | 36.051
7 | 969.86 | 0.198 | Greater |  | 50.130 | 36.051
6 | 1212.6 | 0.247 | Greater |  | 49.140 | 36.051
5 | 1456.15 | 0.269 | Greater |  | 48.700 | 36.051
4 | 1700.11 | 0.315 | Greater |  | 47.770 | 36.051
3 | 1944.94 | 0.360 | Greater |  | 46.860 | 36.051
2 | 2196.97 | 0.407 | Greater |  | 45.910 | 36.051
1 | 2452.24 | 0.454 | Greater |  | 44.960 | 36.051
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
Width-Thickness Ratio Inspection

## Slide 21: Section Inspection 05
Strong Column and Weak Beam
“

## Slide 22: Strong Column/Weak Beam Inspection
Story |  |  |  | 
MRF | 6-10F | 252125~274615 | 215933 | 1.167~1.271
 | 1-5F | 238504~268739 | 215933 | 1.104~1.244
Gravity Frame | 6-10F | 45513~57336 | 30491 | 1.492~1.880
 | 1-5F | 40483~53935 | 30605 | 1.322~1.762
Story |  |  |  | 
MRF | 6-10F | 252125~274615 | 215933 | 1.167~1.271
 | 1-5F | 238504~268739 | 215933 | 1.104~1.244
Gravity Frame | 6-10F | 45513~57336 | 30491 | 1.492~1.880
 | 1-5F | 40483~53935 | 30605 | 1.322~1.762
PASS!
PASS!
PASS!
PASS!

## Slide 23: Design Details 06
Width-Thickness Ratio Inspection
Doubler Plate
Continuity Plate
Connection Size
“

## Slide 24: Doubler Plate
Story |  |  |  |  | Doubler Plate (in.) | Lower Limit
MRF | 6-10F | 4192.271 | 2052.000 | 3.481 | 1.981 | 0.707
 | 1-5F | 4192.271 | 2080.800 | 3.454 | 1.954 | 0.707
Gravity Frame | 6-10F | 2169.962 | 1685.664 | 2.740 | 0.960 | 0.242
 | 1-5F | 2169.227 | 1675.544 | 2.578 | 0.918 | 0.260
Story |  |  |  |  | Doubler Plate (in.) | 
MRF | 6-10F | 4192.271 | 2052.000 | 3.481 | 1.981 | 0.707
 | 1-5F | 4192.271 | 2080.800 | 3.454 | 1.954 | 0.707
Gravity Frame | 6-10F | 2169.962 | 1685.664 | 2.740 | 0.960 | 0.242
 | 1-5F | 2169.227 | 1675.544 | 2.578 | 0.918 | 0.260
PASS!
PASS!
PASS!
PASS!

## Slide 25: Continuity Plate
Story |  |  |  | Design Width
 |  | Lower Limit | Upper Limit | 
MRF | 6-10F | 8.25 | 14.25 | 9
 | 1-5F | 8.25 | 15.25 | 9
Story |  |  |  | Design Width
 |  | Lower Limit | Upper Limit | 
MRF | 6-10F | 8.25 | 14.25 | 9
 | 1-5F | 8.25 | 15.25 | 9
Story |  | Lower Limit |  | Design Thickness
MRF 1-10F | Int. |  | 1.312 | 1.5
 | Ext. | 0.875 |  | 0.9
Story |  | Lower Limit |  | Design Thickness
MRF 1-10F | Int. |  | 1.312 | 1.5
 | Ext. | 0.875 |  | 0.9
Story |  | Width (in.) | (in.) | Full Depth (in.)
MRF 1-10F | Int. | 9 | 1.5 | 31.2
 | Ext. | 9 | 0.9 | 31.2
Story |  | Width (in.) |  | Full Depth (in.)
MRF 1-10F | Int. | 9 | 1.5 | 31.2
 | Ext. | 9 | 0.9 | 31.2
Design Configuration:
Two plates
Two plates
PASS!
PASS!
PASS!
PASS!

## Slide 26: Connection Size
Column:
1. Column Depth = 36in. ≦ 36in.
Beam:
1. Beam Depth = 36in. ≦ 36in.
2. Beam flange thickness = 1.75 in. ≦ 1.75in.
3. The clear span-to-depth ratio = 7.661 in. ≧ 7in.
Limitations
RBS Size:
0.5bbf =9 ≦ a ≦ 0.75bbf =13.5
0.65d =23.5 ≦ b ≦ 0.85d =30.6
0.1bbf =1.8 ≦ c ≦ 0.25bbf =4.5
Reduced Beam Section, RBS
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
PASS!
Selection: a = 9 in., b = 24 in., c = 4.5 in.
Width-to-thickness ratios:
Satisfy the requirements of AISC code
PASS!

## Slide 27: Modal Analysis 07
Structural Period
Structural Mode
“

## Slide 28: Structural Period
Case | Mode | Period (sec) | Frequency (cyc/sec) | CircFreq (rad/sec) | Eigenvalue (rad2/sec2)
Modal | 1 | 1.187 | 0.842 | 5.293 | 28.079
Modal | 2 | 1.185 | 0.844 | 5.304 | 28.137
Modal | 3 | 0.755 | 1.324 | 8.320 | 69.213
PASS!

## Slide 29: Structural Mode
X Direction
Mode 2
Y Direction
Mode 1
Torsion
Mode 3

## Slide 30: Story Drifts 08
“

## Slide 31: Story Drifts
X Direction
Y Direction
PASS!
PASS!
The maximum inter-story drifts both occur on the fourth floor.

## Slide 32: Nonlinear PUSHOVER Analysis 09
PUSHOVER Curve
Story Drifts
Plastic Hinge Distribution
“

## Slide 33: PUSHOVER Curve
X-Dir
Y-Dir
Set the plastic hinges at the relative positions of the 0.05 and 0.95 members of the beam and column.
1. V=1825.573 kips
X & Y lateral disp.=2.799 in.
2. X & Y lateral disp.=18 in.
Strength decrease
  Roof drifts of 1.15% rad
  18in.
  62.4in.
Lateral Disp.=18 in.
Lateral Disp.=18 in.
×4% = 1.15%
V=1825.573 kips

## Slide 34: Story Drifts
X Direction
Y Direction
The maximum inter-story drifts both occur on the fourth floor.
(Roof drifts of 2% rad)
MAX
MAX

## Slide 35: Story Drifts
X Direction
Y Direction
The maximum inter-story drifts both occur on the fourth floor.
(Roof drifts of 4% rad)
MAX
MAX

## Slide 36: Plastic Hinge Distribution (X-Dir)
No plastic hinge
0.5%
1%
1.5%
2%
4%
Plastic hinge occurs on 1st to 6th floors
→ Strength decrease before reaching 1.5%
10th floor
no plastic hinge

## Slide 37: Plastic Hinge Distribution (Y-Dir)
0.5%
1%
1.5%
2%
4%
Same distribution
as X-dir

## Slide 38: Nonlinear Time History Analysis 10
Maximum Inter-Story Drift
Maximum Floor Acceleration
Floor Shear Distribution
“

## Slide 39: The design-based level of appropriate scaled ground motions.
475 year return period spectrum
original acc.
original acc.
X-Dir
Y-Dir

## Slide 40: Maximum Inter-Story Drift
X Direction
Y Direction
MAX
MAX

## Slide 41: Maximum Floor Acceleration
MAX
MAX
X-Dir
Y-Dir

## Slide 42: Floor Shear Distribution
X-Dir
Y-Dir

## Slide 43: Discussion & Suggestion 11
“

## Slide 44
When the lateral displacement of the top floor reaches 2%, plastic hinges appear at the bottom of the columns on the second floor, which shows that the strength of the columns is insufficient. It is recommended that the cross-section be enlarged to improve its strength.
The stress ratio of the section is smaller than that of other parts, and most of them are shown in light blue on ETABS, which means that our section design this time is conservative and less economical.
To ensure that the inter-story drift doesn’t exceed the limit of 0.00341, the columns and beams are designed with large sections. It is recommended to use a Special Concentrically Braced Frame (SCBF) for a more economical design.
Discussion & Suggestion

## Slide 45: THANKS!